## Slide 1: Diamond DA40 KAP 140 Autopilot
Blue Sky Aviation Association, Inc
Notes: We are going to talk about MACA, Joint Operations, and Mission Approval
This is not complicated. I Promise

## Slide 2: Overview
Equipment overview
Limitations
In-flight use
  Climb out
  Level off - Cruise
  Approach
  Missed approach
Effects of Equipment Failure

## Slide 3: Controls and Indications
BARO
ARM
UP
DN
AP
HDG
NAV
APR
REV
ALT
P
R
HDG
AP
ALT
P
T
500
ALERT FT
BENDIX/KING
KAP 144
Autopilot engage/disengage button
  Must be pressed and held
  Turns AP on in default ROL (wing leveler) and VS mode
  Turns AP off

## Slide 4: Controls and Indications
BARO
ARM
UP
DN
AP
HDG
NAV
APR
REV
ALT
P
R
HDG
AP
ALT
P
T
500
ALERT FT
BENDIX/KING
KAP 144
Heading mode selector button
  Selects heading mode
  Turns airplane to maintain heading under heading bug
  Used to toggle between ROL and Heading mode

## Slide 5: Controls and Indications
BARO
ARM
UP
DN
AP
HDG
NAV
APR
REV
ALT
P
R
HDG
AP
ALT
P
T
500
ALERT FT
BENDIX/KING
KAP 144
Navigation mode selector button
  Automatic capture of and tracking of VOR, LOC, or GPS signals set on HSI
  Recommended for enroute navigation

## Slide 6: Controls and Indications
BARO
ARM
UP
DN
AP
HDG
NAV
APR
REV
ALT
P
R
HDG
AP
ALT
P
T
500
ALERT FT
BENDIX/KING
KAP 144
Approach mode selector button
  Capture and tracking of VOR, GPS, LOC and GS on ILS
  Recommended for instrument approaches

## Slide 7: Controls and Indications
BARO
ARM
UP
DN
AP
HDG
NAV
APR
REV
ALT
P
R
HDG
AP
ALT
P
T
500
ALERT FT
BENDIX/KING
KAP 144
Back course approach mode selector button
  Capture of back course LOC
  Response to LOC is reversed (*set the front course)
  Only active when LOC freq is loaded

## Slide 8: Controls and Indications
BARO
ARM
UP
DN
AP
HDG
NAV
APR
REV
ALT
P
R
HDG
AP
ALT
P
T
500
ALERT FT
BENDIX/KING
KAP 144
Altitude hold mode selector button
  Toggles between ALT HOLD and VS mode

## Slide 9: Controls and Indications
BARO
ARM
UP
DN
AP
HDG
NAV
APR
REV
ALT
P
R
HDG
AP
ALT
P
T
500
ALERT FT
BENDIX/KING
KAP 144
Vertical speed mode buttons
  Action of button depends on AP mode when selected
  When in VS mode, momentary press will show captured VS
  Subsequent presses will change target VS by 100 ft.. per min
  When established at an ARMed altitude, a momentary cycle will adjust the ARMed altitude 20 ft. (display will not change)

## Slide 10: Controls and Indications
BARO
ARM
UP
DN
AP
HDG
NAV
APR
REV
ALT
P
R
HDG
AP
ALT
P
T
500
ALERT FT
BENDIX/KING
KAP 144
Altitude Arm button
  Toggles altitude capture on (ALT ARM annunciated) and off
  When armed AP will capture altitude displayed in alerter, if the current VS will direct an intercept.
  Upon capturing altitude, the AP is armed for a new altitude

## Slide 11: Controls and Indications
BARO
ARM
UP
DN
AP
HDG
NAV
APR
REV
ALT
P
R
HDG
AP
ALT
P
T
500
ALERT FT
BENDIX/KING
KAP 144
Barometric pressure button
  Push to display baro setting.
  Large and small knobs are then used to set the desired
  current barometric pressure

## Slide 12: Controls and Indications
BARO
ARM
UP
DN
AP
HDG
NAV
APR
REV
ALT
P
R
HDG
AP
ALT
P
T
500
ALERT FT
BENDIX/KING
KAP 144
Rotary Knobs
  Used to set the altitude alerter
  After pressing BARO button, knobs are used to set current barometric pressure

## Slide 13: Controls and Indications
BARO
ARM
UP
DN
AP
HDG
NAV
APR
REV
ALT
P
R
HDG
AP
ALT
P
T
500
ALERT FT
BENDIX/KING
KAP 144
Altitude Alerter/vertical speed/BARO setting display
  Displays altitude for altitude alerter. This is the ARMed altitude, chime sounds when 1000ft and 200 ft. from altitude
  Shows captured or set VS after pressing UP/DN key
  Shows BARO setting after pressing BARO

## Slide 14: Controls and Indications
BARO
ARM
UP
DN
AP
HDG
NAV
APR
REV
ALT
P
R
HDG
AP
ALT
P
T
500
ALERT FT
BENDIX/KING
KAP 144
Pitch Trim annunciator
  Indicates direction of trim
  Flashes if trim is not satisfied in 10 seconds
  Solid PT without an arrow is an indication of a fault

## Slide 15: Controls and Indications
BARO
ARM
UP
DN
AP
HDG
NAV
APR
REV
ALT
P
R
HDG
AP
ALT
P
T
500
ALERT FT
BENDIX/KING
KAP 144
Autopilot engagement annunciator
  On whenever AP is on
  Flashes during pilot initiated or automatic disconnect

## Slide 16: Controls and Indications
BARO
ARM
UP
DN
AP
HDG
NAV
APR
REV
ALT
P
R
HDG
AP
ALT
P
T
500
ALERT FT
BENDIX/KING
KAP 144
Pitch (P) and Roll (R) axis annunciator
  Indicates failure of illuminated axis
  In turbulent air P may illuminate during abnormal accelerations

## Slide 17: Controls and Indications
BARO
ARM
UP
DN
AP
HDG
NAV
APR
REV
ALT
P
R
HDG
AP
VS
P
T
3500
ALERT FT
BENDIX/KING
KAP 144
ALT
ARM
Top row: Shows what is active
Bottom row: Shows what is armed
ARM
NAV

## Slide 18: Limitations
Maximum flaps 10 degrees
Must be disengaged below 200 ft. AGL on approach, and below 800 ft. for other phases of flight
AP must be off for T.O. and landing
AP preflight required before use of electric trim
De-energize AP if “PITCH TRIM” warning light illuminates

## Slide 19: Preflight
BARO Setting flashing – Set current local barometer
Autopilot - Engage
Flight Controls – Move (Ensure autopilot can be overpowered
A/P DISC/TRIM Switch – Push (Autopilot disengages warning tone heard)
Elevator Trim- Set for take off
Before Takeoff Check
  A/P DISC/TRIM Switch – Push
  BARO –Set
  ALTITUDE Select – Set
If autopilot test fails the airplane may be flown if the Autopilot Circuit Breaker is opened
Use knobs to select level off altitude in Altitude Alerter for first altitude desired

## Slide 20: After Takeoff Climb
Trim aircraft and set stable airspeed and climb
After 800 ft. AGL and wings level, turn on AP by pressing AP button
  AP will be in ROL and VS mode and displayed on face plate
Momentarily press UP/DN key to display captured VS rate
  AP will capture the rate at the time the AP is turned on
  A high climb rate could lead to a stall
  Adjust the VS rate as required by pressing UP or DN as required
Use knobs to select level off altitude in Altitude Alerter (should be set before TO)
Arm Altitude Alerter by pressing “ARM”
Turn HSI heading bug to desired intercept heading (may be set before TO)
Press HDG button to turn to desired heading
Press CDI soft key on GPS as required to select desired Nav mode (VLOC or GPS)
Press NAV key to arm AP to capture and fly the desired course

## Slide 21: Indications During After Takeoff Climb
BARO
ARM
UP
DN
AP
HDG
NAV
APR
REV
ALT
P
R
ROL
AP
VS
P
T
3500
ALERT FT
BENDIX/KING
KAP 144
Press AP button
to turn on autopilot
ROL (roll mode) or
wing level mode
VS (vertical speed)
Captures rate of climb
when AP was turned on
Altitude set in
Altitude Alerter
(Level off altitude)

## Slide 22: Indications During After Takeoff Climb
BARO
ARM
UP
DN
AP
HDG
NAV
APR
REV
ALT
P
R
ROL
AP
VS
P
T
500
ALERT FT
BENDIX/KING
KAP 144
Momentarily press
UP or DN button
Momentarily displays the
captured rate of climb/descent

## Slide 23: Indications During After Takeoff Climb
BARO
ARM
UP
DN
AP
HDG
NAV
APR
REV
ALT
P
R
ROL
AP
VS
P
T
3500
ALERT FT
BENDIX/KING
KAP 144
ALT
ARM
Press ARM to arm the AP to
level off at the preset “Altitude
Alerter” (level off) altitude
ALT ARM will be displayed
to show the AP is armed to
capture the preset altitude
Altitude Alerter (level-off)
altitude

## Slide 24: Indications During After Takeoff Climb
BARO
ARM
UP
DN
AP
HDG
NAV
APR
REV
ALT
P
R
HDG
AP
VS
P
T
3500
ALERT FT
BENDIX/KING
KAP 144
ALT
ARM
Press HDG to make the AP turn
to the heading under the heading
bug on the HSI
Display will switch from ROL to HDG
and aircraft will turn to selected heading

## Slide 25: Indications During After Takeoff Climb
BARO
ARM
UP
DN
AP
HDG
NAV
APR
REV
ALT
P
R
HDG
AP
VS
P
T
3500
ALERT FT
BENDIX/KING
KAP 144
ALT
ARM
ARM
Press NAV button to arm
NAV capture
NAV
NAV ARM will be displayed
showing that the AP is armed
to capture and intercept the
course selected on the HSI

## Slide 26: Indications During After Takeoff Climb
BARO
ARM
UP
DN
AP
HDG
NAV
APR
REV
ALT
P
R
NAV
AP
VS
P
T
3500
ALERT FT
BENDIX/KING
KAP 144
ALT
ARM
Indicator will change from HDG to NAV
when the HSI course is captured
NAV ARM will disappear when the
course is captured

## Slide 27: Indications During After Takeoff Climb
BARO
ARM
UP
DN
AP
HDG
NAV
APR
REV
ALT
P
R
NAV
AP
ALT
P
T
3500
ALERT FT
BENDIX/KING
KAP 144
Desired level off altitude
VS changes to ALT to show the
preset altitude has been captured
ALT ARM is extinguished
when the preset altitude
is captured

## Slide 28: Level off- Cruise
After level off, prior to approach and throughout flight, reset baro setting. Reset altitude select/altitude alerter altitude to the next desired altitude.
  ARM does not have to be reselected
If an enroute climb or descent is required, select VS mode by pressing ALT key (Toggles the AP from capture of the current altitude and VS mode).
  Use UP/DN key as needed to select the desired rate of climb .
During a climb in the VS mode, the current altitude can be captured by pressing the ALT key regardless of what is set in the altitude select/alerter

## Slide 29: Indications after Level Off
BARO
ARM
UP
DN
AP
HDG
NAV
APR
REV
ALT
P
R
NAV
AP
ALT
P
T
3000
ALERT FT
BENDIX/KING
KAP 144
ALT
ARM
Set the next desired altitude
(normally IAF altitude)
ALT ARM will be displayed
showing the AP is armed to
capture the next altitude
Note: ARM is not pressed
ALT is still displayed showing
that the previous altitude is
still captured

## Slide 30: Indications During Descent
BARO
ARM
UP
DN
AP
HDG
NAV
APR
REV
ALT
P
R
HDG
AP
VS
P
T
-300
ALERT FT
BENDIX/KING
KAP 144
ALT
ARM
ARM
APR
Press ALT to toggle
to VS mode
VS displayed
Press DN key to select
desired rate of descent
Rate of descent
momentarily displayed

## Slide 31: Approach
Select approach mode with APR key. (tightens hold and capture parameters)
When the CDI is switched from GPS to VLOC (or vice versa) the AP will revert to ROL mode. (Flashing NAV or APP) Re-select APP with appropriate Nav mode selected
Non-precision approach
  Set MDA in Altitude Alerter
  At FAF, select VS mode by pressing ALT key
  Select descent rate with DN key
  After leveling at pre-selected Altitude Alerter altitude, MDA can be fine tuned with UP/DN key (20 ft. change with each momentary press)
ILS approach
  Pre-select missed approach alt in Altitude Alerter
    Autopilot will capture and follow the ILS glide slope
  Disengage AP at DH

## Slide 32: Indications During Approach
BARO
ARM
UP
DN
AP
HDG
NAV
APR
REV
ALT
P
R
HDG
AP
ALT
P
T
2995
ALERT FT
BENDIX/KING
KAP 144
ALT
ARM
ARM
APR
Press BARO to reset
Altimeter setting
Attitude display switches
to display the
barometric pressure
Use knob to select the desired
Altimeter setting

## Slide 33: Indications During Approach
BARO
ARM
UP
DN
AP
HDG
NAV
APR
REV
ALT
P
R
HDG
AP
VS
P
T
3000
ALERT FT
BENDIX/KING
KAP 144
ALT
ARM
HDG is used to fly holding or the
“Barb” (course reversal) on a
procedure turn
APP ARM will be displayed to show the AP is armed to
intercept the final approach course
(AP will fly tighter tolerances in APP mode)
ARM
APR
Press APR to arm the APP
mode

## Slide 34: Indications During Approach
BARO
ARM
UP
DN
AP
HDG
NAV
APR
REV
ALT
P
R
NAV
AP
VS
P
T
3000
ALERT FT
BENDIX/KING
KAP 144
ALT
ARM
The autopilot will revert to ROL mode if the navigation
source is switched (manually or automatically) from GPS
or VLOC or vice versa. HDG or APR mode as desired
will have to be re-selected and/or armed.
Note: The NAV or APR indicator will flash

## Slide 35: Indications During Approach - GPS
BARO
ARM
UP
DN
AP
HDG
NAV
APR
REV
ALT
P
R
NAV
AP
VS
P
T
3000
ALERT FT
BENDIX/KING
KAP 144
ALT
ARM
During a GPS approach, when you are turned on course to the FAF (Track and Desired Track are within 10°), a message will prompt you to enable the autopilot outputs before using the autopilot for an approach: “APR Guidance Available Use PROC before A/P APR”. Press the procedure (PROC) button and the curser defaults to “Enable A/P APR Outputs?” Press enter (ENT) to provide vertical and lateral GPS approach guidance to the autopilot. Now select approach (APR) on the autopilot. The autopilot will capture both the lateral course and the GPS glidepath.

## Slide 36
Indications During Approach - GPS

## Slide 37: Indications During Approach - GPS
Three Step Summary (the “MPA flow”)
  MSG (read the message)
  PROC (select and accept the Procedure prompt)
  APR (arm Approach on the autopilot)
BARO
ARM
UP
DN
AP
HDG
NAV
APR
REV
ALT
P
R
APR
AP
ALT
P
T
3000
ALERT FT
BENDIX/KING
KAP 144
GS
ARM

## Slide 38: Indications During ILS Approach
BARO
ARM
UP
DN
AP
HDG
NAV
APR
REV
ALT
P
R
APR
AP
ALT
P
T
3000
ALERT FT
BENDIX/KING
KAP 144
GS
ARM
The glide slope will arm as soon as the LOC final
approach is captured and a valid ILS glides slope is
received . At glide slope intercept, ARM goes out and
GS replaces ALT or VS on the top line.
Note: Hold 90 KIAS minimum on approach (recommended)

## Slide 39: Missed Approach
GNS 530 suspends automatic sequencing of waypoints at the missed approach, SUSP soft key is displayed
Disconnect the AP to execute a missed approach
Press CDI soft key on GNS 530 if required to select desired navigation source
  Nav source will normally have to be changed back to GPS to fly procedure
Press SUSP soft key on GNS 530 to start sequencing of missed approach procedure
  Ensure altitude restrictions of the published missed approach are followed before sequencing the missed approach procedure in the GPS
  Do not engage AP below 800ft AGL
Set missed approach altitude into Altitude Alerter
  Missed Approach altitude should already be set in Altitude Alerter during an ILS approach
After start of missed approach follow the same procedures as climb out

## Slide 40: Effects of Equipment Failure
  Failure of Attitude Indicator – No effect
  Failure of DC turn coordinator - Autopilot disengages
  Failure of HSI – No heading signal so ROL mode only
  Failure of Transponder pressure encoder - Altitude alerter/preset fails
  Failure of Trim servo – Auto pilot provides warning tone and disconnects – Manually control aircraft and then Press red dis-engage button to silence tone and pull autopilot circuit breaker

## Slide 41
Adapted from Internet available presentation by:
  Mike Prusak LtCol USAF (ret)
  CAP-USAF STATE DIRECTOR
  CAWG